## Slide 1: Modélisation des gisements miniers - Mining geomodelling -
TD 1 – Stratigraphic & Structural Modeling
Implicit vs Explicit Approach
Lou Declercq

## Slide 2: Exercise 1
Open « TD1_MODELISATION.sprj »
Observe available data
Approach 1 : Explicit modelling
  Build the differents horizons using curves / constraints (at least one)
  Manage horizons erosion by topography surface
  Refine obtained surfaces
Approach 2 : Implicit modelling
  Build a stratigraphic column
  Use SnS (Structure & Stratigraphy Workflow)

## Slide 3: I. General reminders
Open/Create a project
User interface
Object Tree
Object types
Features

## Slide 4: I. Open & Create Projects
When starting a project, be careful with :
Depth axis orientation
Units
Coordinates systems
Selection of add-ons : here ensure you have Structure & Stratigraphy and Reservoir Properties (+ Geoscience Core)

## Slide 5: I. SKUA-Gocad UI

## Slide 6: I. Object Tree
Objects : tall objects sorted by Features
1. Object Tree : Activate/Deactivate diffrents views using tabs
Lists : all objects as a list
Unassigned Objects: all object without features
Properties : all properties on all objects (also available from objects directly)
Ressources : other ressources (classifications, variograms, stratigraphic columns, histograms, …)
2
2
1

## Slide 7: I. Objects types

## Slide 8: I. Objects
Objects; assigned objects to a feature
faults
Stratigraphic models
horizons
Voxets / 3D volumes
Seismic data
2D voxets, maps, images…
Limits, prospects zones
Geological grids
Wells
For each Feature : assigned objects
For each object : properties related, regions, …

## Slide 9: I. Assign features
2. Button « Assign an Objet to a feature »
A
B
C
D
E
E1
D1
Table with unassigned objects
Table of unassigned markers (in wells)
Feature type selection menu (fault, horizon, boundary, etc.)
Fault assigned objects, d1: transfer menu between non-assigned & faults; feature creation & deletion
Same but with horizons

## Slide 10: I. Contextual menu in 3D viewer
Right click on an Object
Display parameters (colors, mesh, nodes…)
Display properties on Object
Hide/Show
Assign Features
…

## Slide 11: I. 2nd contextual menu
Displayed in bottom left corner when object is clicked in 3D view
Display parts
Display parameters
Change color
Display nodes
Transparency
Display mesh
Display borders

## Slide 12: I. Property bars
An option bar appears at the bottom when a property is displayed
Change colormap
Change clipping values
Draw isovalues

## Slide 13: I. One example of restyling topography
Right-click
Trace isolines

## Slide 14: I. Help menu
Direct access via Help

## Slide 15: II. EXPLICIT MODELING APPROACH
Create objects
Edit objects
Cut surfaces
Set constraints / Interpolate surfaces
Cut surfaces
QC

## Slide 16: II. Create objects; edit objects
Every kind of SKUA-Object has its own contextual command menu
Create this kind of object from several type of data
Edition tools
Property Editor
Region Editor
Computation tools…

## Slide 17: II. About object vocabulary
Parts : if object is split in several parts (ex: surface by another)
Regions : area of interest in an object defined by user
Nodes : mesh nodes
Triangle (object mesh elements)

## Slide 18: II. About Constraints
Constraints can be applied between object to fit one to the other

## Slide 19: II. Interpolation of surfaces using constraints
Then you can interpolate surface using these constraints

## Slide 20: II. Edition tools : refine surfaces
Tools commands in object menu
Example:
Split => split mesh in smaller éléments
Beautify: try to respect equilarity of mesh triangles

## Slide 21: II. Erosion ? What about cutting surfaces ?
If you want to take erosion into account you’ll have to cut your surface by your topography
Part 1
Part 2
Part 3

## Slide 22: II. Create a volumetric model from surfaces
When you have created your surfaces => you can create a geological grid
Create a new Voxet
Add Surfaces to the Voxet
Build the model

## Slide 23: II. Quality control on your surfaces
Significant variation of layer thickness due to lack of data
Strategy 2:
Move individual nodes to the desired position (as arbitrary than drawing a cross section)
Set them as Control Nodes
Re-interpolate
Strategy 3:
Use Thickness or Range Thickness constraints NB: thickness is signed (negative above the reference surface)
Strategy 1:
Add interpretive data (hinge lines, cross-sections…)
Reinterpolate

## Slide 24: III. IMPLICIT MODELING APPROACH
Create a stratigraphic column
Workflow SnS
Build Geologic grid

## Slide 25: Workflow SnS
2.Define VOI
1.Input data
3.Build stratigraphic & structural model
5.Build Reservoir grid
4.Generate Fault blocks

## Slide 26: III. Create a stratigraphic column
Or
Create a stratigraphic column: ! Your data must be stored in Features
Aim is to define relationships between your stratigraphic elements

## Slide 27: Relationships between Horizons
Conformable
Conformable

## Slide 28: III. Worflow SnS
Open the Structure and stratigraphy workflow
SnS workflow steps

## Slide 29: III. Worflow SnS
1.
Select Horizon data (surfaces and/or markers)
Build a Stratigraphic context
Check for unconsistencies

## Slide 30: III. Worflow SnS - Exercise
Select horizon data:
Select only the constraints that are used (not the surfaces)

## Slide 31: III. Worflow SnS
2. Select Fault Data you want to use
+ define Fault types
3. Define a VOI

## Slide 32: III. Worflow SnS - Exercise
2. Select Fault Data you want to use
+ define Fault types
3. Define a VOI

## Slide 33: III. Worflow SnS
4. Build Fault Network & Fault Blocks

## Slide 34: III. Worflow SnS
Modeling Horizons:
Choose confidence on Well Markers
Choose to ignore data close to Faults

## Slide 35: III. Worflow SnS - Exercise
Modeling Horizons:
Choose confidence on Well Markers
Choose to ignore data close to Faults

## Slide 36: III. Worflow SnS
Checking volumes of each horizons

## Slide 37: III. Worflow SnS - Exercise
Checking volumes of each horizons

## Slide 38: III. Worflow SnS
Build the geologic grid: choose what horizons to build, cell size, number of cells, etc.

## Slide 39: III. Worflow SnS - Exercise

## Slide 40: III. Worflow SnS - Exercise

## Slide 41: III. Worflow SnS - Exercise