## Slide 1: Modélisation des gisements miniers - Mining geomodelling -
Application to metallogeny, mining exploration and exploitation :
stakes and methods
Marie-Cécile Febvey
Lou Declercq

## Slide 2: Outline of the course / Schedule
Mining geomodelling course
Mining geostatistics course
Project San Nicolas
Oral & Synthetic report
AF1 | – Analyze and process multi-source data to address a mining exploration problem, given an ore genesis problem
AF2 | – Perform a mineral resource assessment.

## Slide 3: Outline of the course / Schedule
F026
F026
F026
F026
F026
F026
F026
Skua Gocad
Isatis.neo
Oral exam

## Slide 4: Geomodelling course outline
Theory (~1h)
TD1 : Implicit & Explicit Modelling
TD2 : Property Modelling & Ore Body construction
Project : San Nicolas

## Slide 5: Courses main objectives
Understand the role and limits of modelling in geology/mining industry
Know the main workflows of geological modelling
Understand the dedicated vocabulary
Know the main concept of Geostatistics applied to mining geomodelling

## Slide 6: Introduction

## Slide 7: What’s the point behind modelling ?
3D Geological Model of the Sullivan Mine, 1940s
Principle:
Numerical approximation of geological reality
Aim:
Better understand subsurface (phenomena, organization, …)
Sullivan Mine Model
in Skua Gocad
Montsion et al., 2015

## Slide 8: What’s the point behind geomodelling ?
[Pellerin, 2014]
Volumetric representation
Boundary representation

## Slide 9: Numerical geology modelling, what for?
  [Gouache, 2021]
  [Fu, 2009]
  [Kelfoun, LMV]
  [Li, 2018]
Earthquakes
Volcanoes
Floods
Collapses
Risk assessment for natural phenomenon : Understand, monitor & predict hazards
=> frequency, location, flows, intensity, …
STAKE: safety, durability, economy

## Slide 10: Numerical geology modelling, what for?
Natural resources assessment :
  Locate, Estimate, Characterize connectivity of reservoirs
Hydrocarbons
Water
Mineral deposits
[Sinha et al., 2013]
[Tyler, 1988]
[John Wiley and sons, 1990, all rights reserved]
STAKE: resources, profitability, targeting

## Slide 11: modelling in mine cycle life
Pollutants concentration
Evaluate flows
Penalizing factors location and concentration
Determine resources location
Ore extractability
Grades determination
© IAEA

## Slide 12: Geomodelling in mining, what for?
Volumes
Location
Connectivity
Geometry  Structures
1. Orebody characterization
=> Orebody profitability?
Grades
[Marchive & Verlhac, 2017]

## Slide 13: Geomodelling in mining, what for?
2. Uncertainties characterization
Exploration strategy : drilling

## Slide 14: Geomodelling in mining, what for?
3. Design and planning of the mine
[Courtesy of Diavik Diamond Mine]
Orebody?
Penalizing factors?
Gangue?
+ Surrounding infrastructures and possible satellite deposits?

## Slide 15: Mine planification
Shallow orebody with mainly horizontal extension
Deep orebody with mainly vertical extension
Open-pit mine
Underground mine
Needs to characterize orebody geometry to choose mining strategy

## Slide 16: Numerical Geology modelling in Mining, what for ?
[Collet, 2022]
4. Production forecasting
Mine production estimation : ISR (In Situ Recovery)
Fluid flow simulations
Chemical reactions simulations

## Slide 17: Size of Mining Projects
Tailings

## Slide 18: Mining modelling chain in, outs & softwares

## Slide 19: Overview of processes
Field work & data
Geological interpretations
Numerical tools
Numerical models
Many possible models!

## Slide 20: What are the field work input data?
Geological interpretations
Time series
[Zhao, 2016]
[Marchal, 2017]
Well injection, production data
Maps, cross sections, outcrop digitation
Drillcore & samples
[Braga, 2019]
[Martz, 2016]
Geology, Geochemistry & petrophysical data, markers
Geophysical survey
[Nejad, 2021]
[Courtesy of Orano]
EM, seismic, radiometric, resistivity

## Slide 21: Drillcore Data
Continuous log properties: geochemical data, spectral data, gamma-ray
Discrete log properties: fracture degree, argillization, bleaching, but also Au grades (every meter), geochemical data…
Sparse
structural data:
stratigraphy,
faults

## Slide 22: About Data Heterogeneities
Multi-scale: from µm to km
Multi-dimensional: 1D, 2D, 3D, 4D
Various range of uncertainties
Different quality of interpretation

## Slide 23: Well Data Overview
Curvilinear length ≠True trace of wells

## Slide 24: What are the output?
3D geomodels: structural models,
petrophysical grids
Detailing the spatial architecture
of the surbsurface
Highlighting the location and
extension of the orebody
Temporal models, …

## Slide 25: Geomodelling softwares
Petrel
Leapfrog
Geomodeller
Surpac Vision
SKUA-Gocad
Isatis Neo

## Slide 26: About Leapfrog
Commonly used geomodelling software in mining industry
Project tree: where objects are stored, created and imported
View selector: where you select objects you want to display (after drag and drop to view area) + display parameters
3d viewer
View bar: slicer, view selection, measurements

## Slide 27: Project tree
To import, create or vizualize objects: go to the right category and click on it
New estimation
Import data
New model

## Slide 28: Access table
Pros:
Easy to use
Basic geostatistic tools
Modern UI
Cons:
Only deterministic approaches
Only Mining (the whole point for Leapfrog)

## Slide 29: Isatis.neo
Geostatistics software (second part of the week)
Pros:
Easy to use
Modern UI
Complete geostatistic tool
Easy bridge to other software
Cons:
Not a modelling software

## Slide 30: Petrel and Eclipse
Petrel: Petroleum modelling software
Eclipse: Fluid flow simulation tool

## Slide 31: SKUA Gocad (Aspen Gocad)
Generic modelling tool (but mostly petroleum)
Pros:
Huge amount of functionalities
Good demonstration tool
Cons:
Hard to manage
Old software

## Slide 32: Short Gocad Story
T-Surf Corp is created
Prof. Mallet (Nancy School of Geology) discovers a new interpolation technique
Gocad Consortium 1
C++ version
2002
Version 2
1988
1995
1998
Earth Decision
Sciences
C Version
Gocad Consortium 3
Pradigm
Gocad Consortium 2
2006
Version 2.2

## Slide 33: SKUA Gocad
Gocad software created at ENSG in 1989
Spin-off company in 1997
Ongoing research at ENSG / GeoRessources:
  Gocad Research Consortium, 12 Companies, 139 universities
Exploration going under cover
  Need for geophysics
  Need for geology, Geophysics and business question integration

## Slide 34: Common Earth Model / Shared Earth Model
Concept From Oil Industry circa 1997
Quantitative model of all available data (drillholes, geophysics, GIS, …)
Shared & Updated model between teams (geophysicists, geomodellers, geologists, chemists, etc.)
Somewhat outdated concept, comes out naturally between branches of a company (especially for geometallurgy)
[McGaughey, 2006]
Or in certain projects (a whole country or a mining district)

## Slide 35: Implicit and explicit modelling

## Slide 36: 2 main types of geomodelling approaches
Explicit Modelling
Implicit Modelling
3D surfaces construction using interpolation between data points: parametric surfaces
Digitation of contacts
Closer to the data
3D surfaces extracted as iso-values of 3D scalar fields: equipotential surfaces
Need a scalar-field
Smooth the data

## Slide 37: 2 main types of geomodelling approaches
[Renaudeau, 2019]

## Slide 38: Implicit modelling with several fields
Using several scalar fields combination to reproduce complex geometry
[Grose, 2021]
[Laurent, 2016]

## Slide 39: Combined approaches
Drillcore data
Simple interpolation
Signed distance field of drillholes
Constrained interpolation
[Zhong, 2019]
Topological robustness (no holes, self-intersection, etc.)
Uncertainties gestion (no constraints => low gradients)
New information added => new surface calculated
Signed distance field function
f=0 : lithological contact
f<0 : inside the volume (ore body)
f>0 : outside

## Slide 40: Modelling workflows steps in mining studies

## Slide 41: Most common geomodelling workflow
From [Mazuyer, 2018]
inversion

## Slide 42: Most common workflow
1. Acquisition of data (on field or remotely)
  Drilling
  Geophysical surveys
  Geological mapping
[www.erdenedrilling.mn]
[www.energymining.sa.gov.au]

## Slide 43: Most common workflow
2. Processing the acquired data
  Analysis of the cores
  Analysis and cleaning of the signals obtained
[Serdoun, 2021]
[Annesley et al, 2013]
[Declercq, 2025]

## Slide 44: Most common workflow
Geological interpretation
  One data set = multiple possibilities
[cours Royer & Caumon 2015]
+ stratigraphic log

## Slide 45: Most common workflow
Structural modeling : understanding fault network and horizons

## Slide 46: Petrophysical modeling
Need of a grid
  A Voxet object is a regularly spaced, 3D grid consisting of volume elements called cells (or voxels).
Petrophysical grid
Structural model
Geostatistical calculations on the grid => the deformation and other structural features are taken into account

## Slide 47: UVT Transform
Transform grid to deposition space
Simple transformation example :
X = Xd
Y = Yd
Z = (Zd – Zmur) / (Ztoit – Zmur)
Xd
Zd
Yd
Deposition space
Actual space

## Slide 48: Regionalization
1. Different data resolutions
2. Different parameter distributions/spatial variations
Global variogram
4
1
3
2
Permeability grid

## Slide 49: Effect on histogram
Global histogram
4
1
2
3
4
1
2
3

## Slide 50: About grids, cells & meshes
Various type of cells :
Various type of grids :
Structured
Unstructured
Hybrids..
regular/irregular connectivity & pattern
Computing efficiency
Geological realism
About regularity

## Slide 51: Petrophysical modelling
  Geostatistics on each region
    Properties can be continuous or categorical
    Methods: estimation or simulation

## Slide 52: Some examples
Indicator kriging (simple)
Nearest neighbour
Indicator kriging (ordinary)
Simulations … (SGS)

## Slide 53: Most common workflow
Numerical simulations
  Need for a specific grid
  Physical simulations: rock stress, flow, wave propagation
[Raguenel et al., RING Meeting 2019]

## Slide 54: Most common workflow
How to draw relevant volumes of interest ? Mean ? Max ? Min ?
=> Dependent on the context
Notion of cut-off (teneur de coupure):
minimal grade for economical profitability
Cut-off = f(market price, extraction cost)
Mine design varies based on the cut-off: several projections must be made during the late exploration stage to prepare for potential variations in commodity prices.
Creation of ore geobodies

## Slide 55: Cut-off
Uranium %
Cut-off 10%
Cut-off 5%
Cut-off 4%

## Slide 56: Most common workflow
Computation of the reserve/resources volumes
  Profitability  Cut-off grade
  Reserves vs resources :
Resources Re
Reserves Rs<Re
Total amount of ore, oil, etc.
present in an area
Initial Re = identified Re + non-profitable Re + non-identified Re +…
Total amount of profitable recoverable resources
Cost of production, market prices, accessibility, etc.
Exploration results
Mine development
Resources
Reserves
Inferred
Indicated
Measured
Probable
Proved
Increasing level of geological knowledge and confidence
Consideration of modifying factors (mining, processing, metallurgical, economical, environmental, social, infrastructural, marketing, governmental…)

## Slide 57: Most common workflow
Block model
  Kind of upscaling: idea is to consider bigger block and not just samples
  Variability on block is smaller than on samples
  Selectivity performed on sample histogram over-estimates reserves
Samples
Block
Average Grade of
Selected Blocks

## Slide 58: Récapitulatif
Notions clefs Cours :
Applications modélisation en Géologie
Applications modélisation en Géologie Minière
Données en entrée d’un logiciel de modélisation
Objets en sortie d’un logiciel de modélisation
Modélisation explicite vs implicite
Common Earth Model
Notion de grille, de cellule, de maillage (+ régulier, irrégulier)
Notion de repères cartésien X, Y, Z vs espace de dépôt U, V, T
Cut-off, ressources, réserves, rentabilité

## Slide 59: Case study San Nicolas vms
Context and Objectives
Lou DECLERCQ
Marie-Cécile FEBVEY

## Slide 60: Objectifs du projet
Work in groups of 3 or 4, mixed between GN & GGMPM students (~1 GN + 2/3 Mines)
Using San Nicolas deposits models & data, estimate ore volumes & grades for different metals. Note that you have to select what data you want to model and justify your choice. Ensure you have listed every data available.

## Slide 61: Acquis d'apprentissage fondamentaux (AF)
AF1 | – Analyze and process multi-source data to address a mining exploration problem, given an ore genesis problem
AF2 | – Perform a mineral resource assessment.

## Slide 62: Deliverable
On Friday 15/11: ~12/15 min presentation by group on Friday 16/01 on how you answer the previous problematic. (AF1)
Report around 5/7 pages maximum for the 30th of January. This report should take the form of a technical report and be as synthetic as possible. (AF2) In this report you should recap the mineral resource assessment. And also detail where you propose to drill new wells and why.

## Slide 63: Key points of your work/presentation:
  Geological contextualisation
  Concerning Cu mineral body, compare different estimations of volumes (using drillholes and density geophysical data as a proxy of the mineralized zone)
  As you have done with Cu property during TDs, compute and fill Ag, Au, Pb and Zn properties in the grid. Justify your choices of interpolation and/or simulation methods, variograms if needed, …
  Compare ore volumes for other metals. Economic grades are 0.5 g/t for Au, and 30 g/t for Ag. Is it worth changing the processing unit to extract Au and Ag in areas mined for Cu (>1.4%Cu) and Zn (> 2% Zn)?
  And what if you change Ag/Au cut-off values?
  What about Pb?
  Where would you drill (< 2500m) to have a better idea of mineable reserves of Cu/Zn? Of Au/Ag?

## Slide 64: VMS deposits (Volcanogenic massive sulfides)
Polymetallic (Cu, Pb, Zn, Fe…) sulfides deposits
Hydrothermal deposits often linked to
underwater volcanic environments
Low volume but high grade
Structural control +++
A geometry that is often quite
complex (+ posterior deformation)
[Galley, 2007]

## Slide 65: VMS deposits (Volcanogenic massive sulfides)
VHMS sample from the Iberian Pyrite Belt
[SGA Student Chapter Prague]

## Slide 66: Geological context
Stratiform Zn-Cu-Ag-Au volcanogenic massive sulfide (VMS)
Located in central Mexico, southern Zacatecas
Late Jurassic-Early Cretaceous
Mineralization age (U/Pb) ~ 148 Ma
Resource estimation: 100 Mt at
  1.36% Cu,
  1.64% Zn,
  0.15% Pb,
  0.41 g/t Au,
  24.0 g/t Ag

## Slide 67: Geological context
Geological setting
Related to a graben-horst – extension – opening of the Gulf of Mexico
The « LaPanza » fault controls the mineralization
Vassalo et al. 2015

## Slide 68: Proposed model for the volcanic structure
Pyritization, chloritization,
sericitization – feldspar and carbonate dissolution -
Vassalo et al. 2015

## Slide 69: Case study
[Vassalo et al. 2015]

## Slide 70
Mafic flows & breccias (XLT) (117,94Ma)
Mafic flow & sediments (MVS)
Massive
Sulfides
(MS or ore)
Rhyolite
Flow-Dome
(146.5 Ma)
(RFD)
Late Triassic Graphitic mudstone
(Gsed)
Mafic volcanics (MVT) (≈149Ma)
Mafic Flows and Tuff (TUF)
Tertiary conglomerates and volcanoclastic breccias (Tcg) (32,3Ma)
Vassalo et al. 2015